## Slide 1: Goddard Sailing Association Hunter 27 Cruiser Qualification Course

## Slide 2: Requirements for Cruiser Helm Qualification
Member of GSA for at least one year and member in good standing for the current year
Qualified Flying Scot Helm
Five successful charters in command of a Flying Scot
Completion of on water qualification card with a qualified cruiser instructor
If born after 1 July 1972, hold Maryland Safe Boating certificate or state approved equivalent.

## Slide 3: Course Overview
Part One – “Take Luck” Systems
Part Two – Sailing Equipment and Procedures
Part Three – Rules of the Road and Emergency Procedures.
Part Four – Piloting and Navigation

## Slide 4: GSA Cruiser Qualification Course
Part One – Take Luck Ship Systems
Version 9

## Slide 5: Part One – Take Luck Ship Systems
Required Equipment
Nav Station / Chart Table
Batteries and battery switch
Cabin lighting and shore power connection
Bilge Pump
VHF radio – radio telephone procedures
Cockpit instrumentation – navigation, depth finder
Running lights
Diesel inboard – motor controls, fuel tank. Operating procedures.
Marine Head and Holding Tank – tank pumping procedures
Galley and Water system

## Slide 6: Required Equipment
Personal Flotation Device (PFD)
  AKA Life Jacket
  1 Per person (appropriate size)
  Plus 1 Throwable
Air Horn
Flares (3): Day & Night
Fire Extinguisher
  Check for in the green!
Trash placard

## Slide 7: Cabin Interior Layout

## Slide 8: Nav Station – Chart Table
Radio
Contains Navigation charts, ships papers, etc.

## Slide 9: Battery Switch
Battery switch has three positions: OFF, ON, ON
  Do NOT switch Batteries while the engine is running
There is also a cigarette lighter socket
Battery Switch shown in OFF position

## Slide 10: DC Power and Cabin Lighting
12 VDC Power Control Panel
(inside next to nav station)
Light Switches
  Cabin Lights
  Running Lights
  Steaming Light (bow lights)
  Anchor Light
Bilge pump switch:
On – overrides float switch
Off – Automatic float switch
(Leave in Off)
External Power Switch
  With shore AC power cord/plug

## Slide 11: Shore Power
110 VAC utility outlets are provided.
110 VAC is provided through the shore power connection and cable
  Make sure the shore power connection is securely fastened. Take a loop around a stanchion or other support so the cable itself is not bearing all the weight.
Shore Power
Connector
Shore Power
Hole for standard extension cord

## Slide 12: VHF radios
Radio License no longer required
Main radio is in the cabin – at the Nav Station, on the chart table.
  Must have main battery switch turned on
  Radio is turned on at the unit.
Hand-held back-up radio in the chart desk (or charging in the shed).

## Slide 13: VHF radio – channels and procedures
Channels
  16 – International Distress and Hailing
  13 – draw bridges, ship to ship
  22A – USCG Liaison
  68, 69, 71, 72, 78A – common working channels
  WX1 – WX7 – NOAA weather
Radio watch – We are not required to carry a radio, but since we do so voluntarily, we are required to guard (listen on) Channel 16 when not using the radio ourselves.

## Slide 14: VHF radio – channels and procedures (2)
Boat to Boat or Marina
  Make initial contact on Channel 16
    (but some marinas monitor channel 68)
  Switch to a working channel: 68, 69, 71, 72, 78A
  Switch back to channel 16 when done
Voice protocol – normal traffic
  “Coast Guard Annapolis, this is sloop Take Luck on channel 22A, Over”
  First Light, this Coast Guard Annapolis, go ahead”
  (State business, “Over”) - back and forth
  (Conclude, “Out, Take Luck switching back to channel 16”)
Voice protocol – Distress Call! – Channel 16
  MAYDAY! MAYDAY! MAYDAY! This is TAKE LUCK, TAKE LUCK, TAKE LUCK, MD 3810 BG one half mile south of the Thomas Point Light. I have a 55 year old male on board experiencing chest pains, request medical evacuation. Three persons total on board. Take Luck is 27 foot sloop, white with black trim. OVER

## Slide 15: Cockpit Instrumentation
Use Power button to turn on
Use Enter button to accept
Use Page button to change chart
Use Direction buttons to scroll
Use Enter button to select
Note: may need to plug in & mount LowRange consol
Plugs are slotted and go in one way only
Don’t use Factory Reset
Use Exit button if stuck

## Slide 16: Magnetic Compasses
Reads magnetic, not true heading.
Magnetic variation in the Chesapeake Bay is about 10° W (i.e. True North (0°) will read 10° on the compass).
Local magnetic variations can differ
Metal on the boat also affects the compass (“Deviation”)
When steering a compass course, note that the boat turns, not the compass! (might be counter-intuitive)
“Right Raise, Left Lower”
Needs power for backlight only.
Hand Compass:
remove & stow compass cover

## Slide 17: Running Lights
Separate qualification required for night operation!
  But in case you are “out” and it gets dark…
Switches are on the DC power panel
“Navigation Lights” are required when underway from sunset to sunrise
  Under sail – side lights (red and green combo on the bow pulpit) and white stern light required
  Under power – side lights, stern light and “steaming light” (forward white – 2/3 way up the mast)
At anchor – 360° anchor light (top of mast) only.
At Anchor
Under Power
Sailing

## Slide 18: Diesel inboard
Diesel inboard motor
  Electric start
  Charges the battery (but slowly)
  Key is located inside cabin – port inside
  Diesel fuel only (starboard)
  Fuel gauge (starboard)
  Half full tank (12 gal. Tank)
    +10 hours running
    0.5-0.6 gal. per hour

## Slide 19: Diesel inboard - 1
Start Key
on position
Gearshift
neutral position
Throttle
off position
Warning Lights (Oil & Alternator)
Come on when start key is on
Go off when motor is running
Set Throttle
10 o’clock position to start engine
Turn Start Key to right
engages starter motor
start engine
Starting position:
Gearshift in neutral
Throttle in idle
(between 9-10 o’clock position)

## Slide 20: Diesel inboard - 2
Reverse
Forward
Throttle up
Cooling Water discharge when motor is running
Throttle back to idle to change gears
To shut down engine
set to Neutral and turn Throttle to off
do not turn key off before engine stops

## Slide 21: Diesel Operation - 3

## Slide 22: Diesel Inboard - 4 Operating procedures
Check fuel level before leaving dock – refill (Charter fee includes fuel)
Set battery switch On
  Do not switch batteries while engine is running!
Set Gearshift to neutral (centered), Throttle to 10 o’clock position.
Insert Key, turn to on, and then to start. When engine fires, check for cooling water discharge from the motor stalk.
  SHUT DOWN IF THERE IS NO COOLING WATER FLOW!
Remove engine key after starting or stopping (to avoid kicking it)
Reduce engine speed to idle (10 o’clock) before shifting gears
To shut down/secure the engine –
  Shift to gearshift to neutral (12 o’clock)
  Set throttle to off (12 o’clock)
  Do not turn key off before engine stops!
  Turn key to off; remove and return to hook in cabin

## Slide 23: Toilet (Head)
Never put anything in the toilet unless you have eaten it first
(marine toilet paper is OK too)

## Slide 24: Toilet (Head) 2 - Operation
Consider whether to add seawater to the bowl before use. If so, switch to “Wet Bowl” and pump handle.
After use, first empty the bowl by pumping the handle in “Dry Bowl” position.
Then move the switch to “Wet Bowl” and pump some more to flush with sea water
Then switch back to “Dry Bowl” and pump out the sea water.
All this goes into the holding tank -- so don’t overfill!
Dry Bowl
Wet Bowl

## Slide 25: Toilet (Head) 3 – Pump Out
Pump out is available at many gas docks
  Chesapeake Bay is a “No Discharge Zone”
Club policy is to empty the holding tank monthly
  But check the tank to make sure it has room
  cost of pump-outs is included in the charter fee, and is reimbursable if you pay.
Pump out fitting on Deck – labeled “Waste” (starboard)

## Slide 26: Toilet (Head) 4 – Tanks & Valves
Holding tank is under the Vee Berth
  Check tank fullness for pump out
  No adjustment need for waste pump out
  Seawater intake for flushing under starboard berth
Waste switch set to Tank
Do not touch!

## Slide 27: Galley
Sink/wash basin
  fresh water drain
  holding tank in bow– not potable
Icebox