## Slide 1: Goddard Sailing Association Hunter 27 Cruiser Qualification Course

## Slide 2: GSA Cruiser Qualification Course
Part Two – Sailing Equipment and Procedures

## Slide 3: GSA Cruiser Qualification Course Part Two – Sailing Equipment and Procedures
Halyards
Roller furling jib
Jib Sheeting -- winches
Main Sheet
Reefing the main
Topping lift
Bimini
Anchoring

## Slide 4: Halyards
Main halyard – raising the mainsail
  Slacken the mainsheet; re-jam
  Release the downhaul (optional)
  Start (and stow) boom locked in top pin position
  Insert the head of the luff rope in the mast slot
  Raise the main from port side using the halyard and run around the winch
  Cleat the halyard at the base of the mast
  Release the track pin, allow the boom to fall
  Snug and cleat the downhaul
Topping Lift
  Check for slack
  Check cleat to mask
Jib halyard
  Check cleat to mask

## Slide 5: Roller furling jib
Jib wraps around the forestay for easy deployment and retraction
Leave the jib halyard up at all times!
Can be used partially-furled in high winds
Controlled by the jib furling line – leads to the cockpit
To unfurl:
  Heading: close reach to broad reach
  Un-cleat the furling line and lay the line out untangled
  Pull out appropriate jib sheet
  Make sure the “lazy” jib sheet is free
To furl
  apply slight “back pressure” to jib sheet
  Pull on furling line
  Continue until jib sheets wrap once around the sail
  Cleat
  In high winds, watch out for a flapping Clew!
Back pressure helps sail / line wrap smoothly

## Slide 6: Jib Sheeting
Port and starboard jib winches – increase sheeting force
  Both winches are the same part
    only turn clockwise
  Winch Handles stored in cabin
  Use a single turn initially, when sheeting in by hand
  Then 3 turns, when using winch handle – apply moderate tension to free end of sheet
  Winches have ratchets – can sheet in by going back and forth
jib furling line

## Slide 7: Main Sheet
Attached aft end of the boom
4:1 Block
Jam Cleat
  Pull down to release
Traveler
  Center upwind
  Ease downwind
Jam Cleat

## Slide 8: Weather Helm
Tendency for boat to turn into the wind
  Especially in strong winds
May require considerable force on the tiller to hold a course
Remedies:
  Slight: Adjust (tighten) backstay
  Moderate or severe: Reduce Sail
    Reef Main
    Partially furl jib
    Either reduction helps weather helm

## Slide 9: Reefing the Mainsail
Head close to the wind
  On either jib or motor
  Ease mainsheet
At the Mast:
  Lower main halyard
  Put Reef Cringle on luff over tack hook
  Tighten halyard
Reef Cringle
  tack hook

## Slide 10
Reefing the Mainsail (2)
Near the end of the boom:
  Ensure the reefing line goes through Leech Cringle
  Tighten the reefing line:
    on aft-boom goes through reef cringle on leech of the sail, through boom to jam cleat forward.
    Serves as outhaul when reefed
Dress sail with lines through reef points
  Optional
  Non load bearing
Shaking out the reef
  Reverse reefing procedure
jam cleat
downhaul

## Slide 11: Other
Topping lift
  Holds boom up when the mainsail is down
  Adjustable at the base of the mast
  Do not sheet against the topping lift!
    Should remain slightly loose
Bimini
  Shades the cockpit

## Slide 12: Mooring Lines
Through chocks in bow
Crossed in the stern

## Slide 13: Anchor Holder
Velcro Fastener
Sets in gripping bracket on rail
Remove/stow deck cover
Let out through port bow chock
Deck cover

## Slide 14: Anchoring
Scope: Ratio of length of line to “vertical” drop from bow to the bottom (at high tide)
  5:1 Lunch Hook
  7:1 Overnight
  10:1 Storm
Spot selection:
  Protected, 360° swinging room
To Anchor:
  Prepare anchor
  Head to wind, dead stop, Drop anchor
  Back away (motor or wind), take a bite to set the anchor
  Let out appropriate scope, cleat
  Anchor Light
  Check for drifting
To leave anchor:
  Get directly above anchor (pull or motor) – anchor line vertical
  Cleat anchor line – the boat’s momentum will free anchor
  Pull up (weigh) the anchor, clean and stow